"Exploring Technology: Creative Constructions for the Environment and the Universe"
Simple Electric Motor
By Georgios Pefkianakis

---
The Science
"Electromagnetism converts electrical energy into mechanical motion through interaction."

---
The Experiment
The Experiment

---
Materials
- Copper wire:
- Battery
- 2 Paper clips
- Magnet
- Electrical tape
Materials
Found around the house!
[Speaker Notes: Copper wire: Acts as the conductor for electrical current. Battery: Provides the electrical energy to drive the motor. Paperclips: Serve as supports and electrical connectors. Magnet: Supplies a static magnetic field. Electrical tape (optional): Ensures stability in the connections.]

---
Construction
Construction
1. Wind the copper wire into a circular coil, leaving enough wire at each end for connection.
2. Strip the insulation from the ends of the wire. To ensure smooth operation, leave the insulation on the bottom half of each end intact to enable intermittent electrical contact, crucial for consistent spinning.
3. Attach the paperclips to the battery terminals, ensuring they are securely connected.
4. Place the coil on the paperclip supports and position the magnet beneath the coil.

---
Hypothesis
Hypothesis

---
We expect the coil will spin continuously in one direction, provided the setup is correct

---
The result
The result

---
Results explained
Results explained
Coil Rotation:When the circuit is completed, the coil rotates due to the interaction between the magnetic field generated by the current and the field from the permanent magnet.
Continuous Motion: Intermittent contact from the partially stripped wire ends ensures the coil spins in a consistent direction, maintaining motion.
Energy Conversion: The experiment successfully converts electrical energy from the battery into mechanical energy, showcasing practical applications of energy transformation.
Understanding of Motor Basics: The experiment serves as a simplified model of electric motors, helping to connect theoretical knowledge to practical applications.

---
Conclusion
Conclusion

---
Conclusion
Conclusion
A simple electric motor is more than just a classroom experiment
A gateway to understanding the relationship between electricity and magnetism, the principles of energy conversion, the materials and processes behind modern technology.
By engaging in such activities, we inspire curiosity, innovation, and a commitment to a sustainable future.